## Slide 1: Summary of Setups, Rules, and Outstanding Questions
Information:
  UVS.Science_Reqs.proposed.191028 is the file where I am getting the requirements info
Rules:
  For the duration of the stares that happen >+/-2 hours (or could define this as when Europa is smaller than the 7.5 deg FOV) from Europa, we cycle through the Activity Definition Cards defined as “distant”.
    Stare activity durations are typically ~1.5 – 2 hours. The three cards developed for aurorae stares total 24 minutes. So we’d cycle through these cards 3 – 4 times per stare.
Concerns/ Questions:
  With the constant recalculating for the spatial bins, will this require regular uploads of the LUTs?
    This is especially true for the C/A science and may need to impact our total integration time, though the only changes are the sampling time and any spectral setup changes we choose to make (the FOV is filled anyway)… does changing the sampling time affect the LUTs?
  Data Volume! Need to run these calculations to see how much data volume this will all cost…
    Maybe we cycle through lower resolution images, etc.
    Or we keep stares as “placed last” in the timeline and
  What do we want for night side observations near C/A? Pippa mentioned just doing counts and putting into housekeeping. But AP on the night side at the very fast sampling times will not likely result in much data, but cost a lot in data volume. Or we accept more smearing.
  We may want to make the same “surface stare” card for HP mode and cycle between those two in case we can get some good high res images.

## Slide 2
UVS_001_AP_SAA | UVS Surface, Aurora, Airglow Stare: Deep, High Spectral Resolution Search |  |  |  | 
Conceptual Description | This observation is for distant (>+/- 2 hours) SAA stares with high spectral resolution across the slit to look for al species, including the N2 LHB band emissions (125 – 220nm), N (124nm, 141 nm, 149 nm), Cl (lines between 118 – 140), Ca (188.3), Mg (182.8), CO (151 and 148 nm) and C (156 nm and 155 nm), and H2 and Werner bands (85 – 165 nm), Sulfur emissions. Acquired in AP mode to collect as many photons as possible, especially with the very high spectral resolution. This example created for when Clipper is ~100,000 km from Europa |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram |  |  |  | 
Scheduling/Avoidance rules | No phase angle dependence. Relevant for day and night because searching for emissions. |  |  |  | 
Time Sampling | 120 s Longer sampling to detect faint emissions, but not too long to miss temporal changes |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | 600 s |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | UVS.005: Atmospheric Spectral Resolution Full Range (2 nm resolution between 60 – 180 nm) |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 258 | 34 + 2 (34 on target, 1 bin above and below) | 30 | 10 | 2 (regions), 10 (spat) 10 (spec)
 | Binning the entire bandpass by 0.6 nm for Nyquist sampling for filled-slit observations | Spatial bins are calculated for AP = (7.5 < (europa angular diameter * 1.5))/0.08 HP = (7.5 < (europa angular diameter * 1.5))/0.03 This gives high spatial resolution 1 Europa radius above and below the limb Europa angular diameter = 2.*atan(Re/distance)*180./PI In this example, Clipper is ~100,000 km from Europa. | Commonly used phd | Long integrations, but looking for very faint sources so moderate well depth chosen | Standard STIM setup

## Slide 3
UVS_002_HP_SAA | UVS Surface, Aurora, Airglow Stare: Auroral Rocking Studies |  |  |  | 
Conceptual Description | This observation is for distant (>+/- 2 hour) snapshot stares of the oxygen and hydrogen aurora large-scale morphology and location, including how they switch between poles depending on Europa’s position in the magnetosphere (e.g., Roth et al. 2016). |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram – HP Resolution chosen to obtain 100 km/pix resolution throughout most of flyby; <90 km/pix (global scale) +/- 5 hours; 50 km/pix (atmosphere resolution at +/- 3.5 hours) |  |  |  | 
Scheduling/Avoidance rules | No phase angle dependence. Relevant for day and night because searching for emissions. |  |  |  | 
Time Sampling | 10 s [ too long for these bright emissions ? ] Large scale morphology not expected to change too rapidly |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | 120 s |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | UVS.006: Plume Search Spectral Resolution (2 nm resolution between 100 – 140 nm) |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 140 | 223 + 2 (223 on target, 1 above and below) | 30 | 12 | 2 (regions), 10 (spat) 10 (spec)
 | 55 nm – 100 nm: (5 bins) 25 nm resolution, sub-sampled by 3 100 nm – 140 nm: (100 bins) Highest filled-slit resolution of 1.2 nm, sub-sampled by 3; resolves Lyman Alpha (121.6 nm) and 2 oxygen lines (130.4 and 135.6 mn) [ do we need more continuum? ] 140 nm – 210 nm: (35 bins) 6 nm resolution, sub-sampled by 3 | Spatial bins are calculated for AP = (7.5 < (europa angular diameter * 1.5))/0.08 HP = (7.5 < (europa angular diameter * 1.5))/0.03 This gives high spatial resolution 1 Europa radius above and below the limb Europa angular diameter = 2.*atan(Re/distance)*180./PI In this example, Clipper is ~40,000 km from Europa. | Commonly used phd | Higher Well Depth due to bright emissions features possible saturation | Standard STIM setup

## Slide 4
UVS_003_HP_SAA | UVS Surface, Aurora, Airglow Stare: Short-term Variability of Auroral Morphology |  |  |  | 
Conceptual Description | This observation is for distant (>+/- 2 hour) short-term variability of auroral morphology. It is intended to have the same setup as the Auroral Rocking Studies, but much shorter sampling time |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram – HP Resolution chosen to obtain 100 km/pix resolution throughout most of flyby; <90 km/pix (global scale) +/- 5 hours; 50 km/pix (atmosphere resolution at +/- 3.5 hours) |  |  |  | 
Scheduling/Avoidance rules | No phase angle dependence. Relevant for day and night because searching for emissions. |  |  |  | 
Time Sampling | 0.10 s Searching for short-term variability in the auroral emissions |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | 600 s |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | UVS.006: Plume Search Spectral Resolution (2 nm resolution between 100 - 140 nm) |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 140 | 223 + 2 (223 on target, 1 above and below) | 30 | 8 | 2 (regions), 10 (spat) 10 (spec)
 | 55 nm – 100 nm: (5 bins) 25 nm resolution, sub-sampled by 3 100 nm – 140 nm: (100 bins) Highest filled-slit resolution of 1.2 nm, sub-sampled by 3; resolves Lyman Alpha (121.6 nm) and 2 oxygen lines (130.4 and 135.6 mn) [ do we need more continuum? ] 140 nm – 210 nm: (35 bins) 6 nm resolution, sub-sampled by 3 | Spatial bins are calculated for AP = (7.5 < (europa angular diameter * 1.5))/0.08 HP = (7.5 < (europa angular diameter * 1.5))/0.03 This gives high spatial resolution 1 Europa radius above and below the limb Europa angular diameter = 2.*atan(Re/distance)*180./PI In this example, Clipper is ~40,000 km from Europa. | Commonly used phd | Moderate well depth because of very short sampling time | Standard STIM setup

## Slide 5
UVS_005_HP_SAA | UVS Surface, Aurora, Airglow Stare: Plume Search |  |  |  | 
Conceptual Description | This observation is for plume imaging, and should occur at a distance of <28,000 km, when we can achieve 30 km/pix resolution in HP mode. Issue: this is right before Europa fills the slit anyway, so probably only a limited time when this can be applied and see a plume on the limb… but could be used for on-disk detection? |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram – HP Resolution chosen to obtain 30 km/pixel resolution to detect plumes |  |  |  | 
Scheduling/Avoidance rules | No phase angle dependence. Relevant for day and night because searching for emissions. These occur once HP mode achieves 30 km/pix for plume detection at < 28,000 km |  |  |  | 
Time Sampling | Time sampling = Projected slit width / Relative Surface Velocity Projected slit width = tan(0.05 deg / 2) * distance For this example at ~20,000 km, time sampling = 30s |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | 60 s [need shorter or longer?] --- need to check notes on this. |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | UVS.006: Plume Search Spectral Resolution (2 nm resolution between 100 – 140 nm) UVS.0024: Spatial resolution shall be < 30 km/pixel at an altitude of 10,000 km or less |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 140 | 250 | 30 | 8 | 2 (regions), 10 (spat) 10 (spec)
 | 55 nm – 100 nm: (5 bins) 25 nm resolution, sub-sampled by 3 100 nm – 140 nm: (100 bins) Highest filled-slit resolution of 1.2 nm, sub-sampled by 3; resolves Lyman Alpha (121.6 nm) and 2 oxygen lines (130.4 and 135.6 mn) [ do we need more continuum? ] 140 nm – 210 nm: (35 bins) 6 nm resolution, sub-sampled by 3 [should be toss shorter and longer bins? This could give us other surface info though? ] | Spatial bins are calculated for AP = (7.5 < (europa angular diameter * 1.5))/0.08 HP = (7.5 < (europa angular diameter * 1.5))/0.03 This gives high spatial resolution 1 Europa radius above and below the limb Europa angular diameter = 2.*atan(Re/distance)*180./PI In this example, Clipper is ~20,000 km from Europa, so slit is filled | Commonly used phd | Moderate well depth because of short sampling time | Standard STIM setup

## Slide 6
UVS_001_AP_CA | UVS Surface, Aurora, Airglow Stare: Closest Approach |  |  |  | 
Conceptual Description | This observation is for surface stares at the time surrounding closest approach. It is a high spatial, low spectral resolution observation, designed for the distance range to acquire 1 km/pix spatial resolution in AP mode. This is approx +/- 200 s from C/A. It is done in AP mode to capture as many photons as possible in the short integrations. |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram |  |  |  | 
Scheduling/Avoidance rules | Phase Angle Requirement boresight < 90 degrees and 60% of slit < 90 degrees Phase Angle Occurs when s/c altitude < 350 km |  |  |  | 
Time Sampling | Time sampling = Projected slit width / Relative Surface Velocity Projected slit width = tan(0.05 deg / 2) * distance |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | 400 s This is the approx. time when AP mode can get 1 km/pix res Do not want to run this mode too long or data volume will explode, but also do not want to change LUTs and lose data |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | UVS.010: Regional Scale Surface Spatial Resolution ( < 1 km/pix) [ Guiding Req ] |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 20 | 94 | 30 | 8 | 0
 | 55 nm – 118 nm: 25 nm resolution, No sub-sampling 118 nm – 140 nm: 3 nm resolution (gets relatively high spectral resolution near solar features (C, H and O) should we lower resolution elsewhere, and get even higher spectral resolution in this region? 140 nm – 210 nm: 6 nm resolution, No sub-sampling | Europa fills the slit, so full AP spatial resolution, subsampled by 2 pixels. | Commonly used phd | Short integrations, so unlikely to saturate | NO STIM for this part of the flyby.

## Slide 7
UVS_002_AP_CA | UVS Surface, Aurora, Airglow Stare: Surface Composition |  |  |  | 
Conceptual Description | This observation is for surface stares for the duration of when Europa has filled the slit, but the spatial resolution is still >1 km/pix |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram |  |  |  | 
Scheduling/Avoidance rules | Phase Angle Requirement boresight < 90 degrees and 60% of slit < 90 degrees Phase Angle Occurs when 350 km < s/c altitude < 24,000 km (filled slit) |  |  |  | 
Time Sampling | Time sampling = Projected slit width / Relative Surface Velocity Projected slit width = tan(0.05 deg / 2) * distance |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | 300 s [ this could allow us to cycle through a lower spectral resolution, lower data volume set, or an HP version of this for higher spatial resolution, or we just keep repeating this observation every 5 min ] |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | [ Planning Guidelines ] UVS.003: Surface Spectral Resolution Bandpass Sub-range #1 UVS.004: Surface Spectral Resolution Bandpass Sub-range #2 |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 108 | 94 | 30 | 10 | 2 (regions), 10 (spat) 10 (spec)
 | 55 nm – 118 nm: 25 nm resolution, sub-sampled by 3 118 nm – 145 nm: Highest filled-slit resolution of 1.2 nm, sub-sampled by 3 145 nm – 210 nm: 6 nm resolution, sub-sampled by 3 | Europa fills the slit, so full AP spatial resolution, subsampled by 2 pixels. | Commonly used phd | Moderate integration time, moderate well depth | Standard STIM

## Slide 8
UVS_003_AP_CA | UVS Surface, Aurora, Airglow Stare: Geological Feature |  |  |  | 
Conceptual Description | This observation is designed to do high spectral resolution imaging when flying over a geological feature of interest as identified by the Geology Working Group |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram |  |  |  | 
Scheduling/Avoidance rules | Phase Angle Requirement boresight < 90 degrees and 60% of slit < 90 degrees Phase Angle Should occur for the duration over which the boresight is over the geological feature + 10 seconds before and after |  |  |  | 
Time Sampling | Time sampling = Projected slit width / Relative Surface Velocity Projected slit width = tan(0.05 deg / 2) * distance |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | Auto-set for duration of fly-over of geological feature + 10 seconds before and 10 seconds after |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | [ Planning Guidelines ] UVS.003: Surface Spectral Resolution Bandpass Sub-range #1 UVS.004: Surface Spectral Resolution Bandpass Sub-range #2 |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 108 | 94 | 30 | 10 | 0
 | 55 nm – 118 nm: 25 nm resolution, sub-sampled by 3 118 nm – 145 nm: Highest filled-slit resolution of 1.2 nm, sub-sampled by 3 145 nm – 210 nm: 6 nm resolution, sub-sampled by 3 | Europa fills the slit, so full AP spatial resolution, subsampled by 2 pixels. | Commonly used phd | Moderate Well Depth since this card can be placed whenever there is a feature (could be relatively higher flyby) | NO STIM for this part of the flyby since this observation is relatively brief

## Slide 9
UVS_004_AP_CA | UVS Surface, Aurora, Airglow Stare: Nighttime Surface Studies |  |  |  | 
Conceptual Description | AP Nightside observation designed to acquire < 100 km/pix spatial resolution surface observations while obtaining the highest SNR. This observation focuses on Lyman-alpha and is therefore lower spectral resolution in other bandpasses. |  |  |  | 
Type | SAA Stare |  |  |  | 
Observation Type | Histogram |  |  |  | 
Scheduling/Avoidance rules | Phase Angle Requirement boresight > 90 degrees and 60% of slit > 90 degrees Phase Angle Occurs when s/c altitude < 36,000 km (filled slit) [ might be good to have a lower limit on this instead of collecting data with extremely short sampling time on the night side] |  |  |  | 
Time Sampling | Time sampling = Projected slit width / Relative Surface Velocity Projected slit width = tan(0.05 deg / 2) * distance |  |  |  | 
Data rate ¦ with overhead |  |  |  |  | 
Total duration | 600 s |  |  |  | 
Total data volume |  |  |  |  | 
UVS Requirements Met | [ Planning Guidelines ] UVS.008: Spatial resolution < 100 km/pixel at <36,000 km altitude UVS.038: global scale nightside stares occur <36,000 km altitude UVS.003: Spectral Resolution Bandpass Sub-range #1 UVS.004: Spectral Resolution Bandpass Sub-range #2 |  |  |  | 
Data Package Information | Spectral Bins | Spatial Bins | Pulse Height (bins) | Bit Well Depth | STIM Regions
 | 34 | 94 | 30 | 8 | 2 (regions), 10 (spat) 10 (spec)
 | Bin all wavelengths < 117 nm into 4 bins (<25 nm resolution). High resolution near Lyman alpha: 117 – 127: 3 bins will Nyquist sample near Lyman alpha. Longer wavelengths 127 – 210, binned to 6 nm resolution (subsampled by 2 pixels) is 28 bins. | Europa fills the slit, so full AP spatial resolution, subsampled by 2 pixels. | Commonly used phd | No saturation concerns [ although if we do catch atmospheric emissions, there could be… ] | Standard STIM

## Slide 10: Discussion with Pippa, Vincent, & Rohini: Close Stares:
Dayside:
  AP when super close (not enough photons in short integration time for longer), HP at some range too
    +/- 300 seconds in E18 that AP gets us <1 km/s res
    +/- 500 seconds in E18 that HP gets us <1 km/s res
    Lower WD for these short integration times (10)
  Max spatial resolution Sampling time --- set by relative surface velocity.
    For E18, this is ~0.1 s for +/- 400 s of C/A
  Need a plume search one that happens at the +/- 3 hour mark or a specific distance.
Nightside:
  Integrate over the whole slit, look at spectra
  Something clever with housekeeping data?
    Count rates at just the Oxygen and LyAlpha lines?
  Need much longer integration times --- maybe better to not waste data volume by not even being on when super close to the surface for most flybys?
    Tommy said we really do need the modeling for this --- how many surface photons are we going to get at diff phase angles?
    Do we just accept smearing of surface?
    JUICE doing fewer of these
    We can also put them lowest priority
Concerns:
  Huge concern with data volume. We’ll need some flybys when we’re prioritizing stellar occs, transits, etc.
  Maybe we only do max resolution C/A when we’re flying over a local feature
    (have an “if” statement in there to set this up)

## Slide 11: Far Stares:
Distant, deep integrations to search for trace species (day & night)
  High spectral resolution --- all the way?
    Pippa to send some example spectra from HST to check for big gaps in spectra where we can be more coarse
    Bin at 0.6 nm for Nyquist sampling
    Maybe can cut the shorter stuff (see where the Warner bands really are and if there are brighter ones at longer wavelengths
  High spatial resolution --- AP probably better
    Spatial resolution auto-set by distance to Europa at the end of the integration period
    Auto-set by distance at the closest point of the stare integration
  Sampling time: 120 s
  10 min integration?
  Well depth?
  Cut these later in the missions if not needed?
Auroral Shifting/Rocking (Day & Night)
  Primarily Oxygen and Hydrogen, some continuum on either side
  High Spatial resolution – HP if far, AP if closer? Auto-define based on distance? AP because of the radiation impacts near Jupiter? Vincent mentions lower SNR on Juno for the higher res slit.
  Sampling time
    Lorenz’ 2016 paper, Kurt mentioned on the order of 30 min or do a 2 min exposure ever hour to show flip flop from pole to pole
  When do we want these done?
    This would be a scheduling thing then. Within each stare period, cycle through the different stare modes, come back to this one every 3 minutes?
More rapid high spectral mode (Day & Night)
  Same as above spatial/spectra
  Spatial res not as critical here.
  Do this over different locations in the magnetosphere to build up map of changes --- doing this snapshot every few hours
  Maybe do from farther
  10 min, with 100 ms sampling of “these lines” --- I think this was referring to O and H still
Others that are missing? Lower resolution/ data vol versions of these? Just put a prioritization on some?
Do we just put a command that cycles through these types of stares?
Concerns about how often we’d need to change the LUTs
  Need to go through a timeline and see how often the LUTS would be updated in this case
  Can we change part of the LUTS without having to upload all new LUTS?
Concerns about data volume